## Slide 1
PFAS Persistence & Technical Challenges
PFAS (per- and polyfluoroalkyl substances) are persistent organic pollutants with extreme chemical stability. These "forever chemicals" resist degradation and accumulate in the environment, requiring specialized remediation approaches.
Half-life in soil:
>50 years
Solubility in water:
High (mobile)
Regulatory limit:
4 ppt (PFOA/PFOS)
PFOS
PFOA
PFBS
PFHxA
PFHxS
Conventional System Limitations
Technology | Short-chain PFAS | Organic Matter | Status
GAC | Poor removal | High fouling | Limited
IX Resins | Breakthrough | Premature fouling | Partial
RO | Effective | Membrane fouling | High cost
PFAS Removal Efficiency Comparison
Long-chain
Short-chain
99.9%
Long-chain removal
95%
Short-chain removal
30 min
Contact time
5-10 cycles
Regeneration
Dynamic column capacities are significantly lower than theoretical batch isotherm results. Scale-up designs must utilize conservative dynamic capacity.
PFAS Remediation Platform
Technical Challenge Overview & Solution Framework
Technical Analysis
Copyright 2026 Shield Nutraceuticals/Chitosan Global
Contact: John Hott
Email: John@Chitosanglobal.com
Website: chitosanglobal.com

## Slide 2
PFAS Remediation Platform
Platform & Mechanisms
Integrated Immobilization Platform
A specialized "treatment train" platform combining mushroom-derived Chitosan Oligosaccharide-Hydrochloride (COS-HCl) with an engineered biochar matrix. This system manages the recalcitrance, mobility, and regulatory stringency of PFAS in soil and water environments.
COS-HCl Specifications
Surface Charge
+71 mV
Deacetylation (DDA)
98%
Molecular Weight
3 kDa
Source
Mushroom-derived
Engineered Biochar
Primary Role
Physical Scaffold
Interaction Type
Hydrophobic
Washout Prevention
Stabilizes Soluble COS
Synergy
Dual Mechanism Action
Dual Mechanism Binding Action
1. Electrostatic Attraction
COS-HCl provides an exceptionally high positive surface charge density (+71 mV). This vigorously attracts and binds anionic (negatively charged) PFAS molecules.
Highly effective for short-chain PFAS (e.g., PFBS, PFHxA)
Addresses breakthrough issues common in traditional systems
2. Hydrophobic Adsorption
The engineered biochar matrix acts as a high-surface-area physical scaffold that captures PFAS molecules via hydrophobic interactions while physically trapping them.
Highly effective for long-chain PFAS (e.g., PFOS, PFOA)
Prevents the highly water-soluble COS-HCl from washing out
Synergistic Scavenger Effect: Together, this composite leverages both mechanisms to effectively immobilize all PFAS variants. By acting as an organic scavenger, it drastically reduces mass flux and mitigates the fouling of costly downstream treatment systems (like GAC or Ion Exchange resins) by naturally occurring organic matter.
Copyright 2026 Shield Nutraceuticals/Chitosan Global
Contact: John Hott | Email: John@Chitosanglobal.com | chitosanglobal.com

## Slide 3
Application Protocol & Dosage Framework
Soil & Water Treatment Implementation Guidelines
Soil Matrix Protocol
Vadose & Saturated Zones
1
Site preparation with high-resolution characterization to define plume boundaries
2
Excavate soils with extreme PFAS concentrations
3
Blend biochar with COS-HCl solution (1:10 to 1:20 mass ratio)
4
Mechanical mixing with rotary mixers in controlled 1-2 ft lifts
Water Matrix Protocol
Groundwater & Stormwater
1
Route liquids to equalization tank
2
Solids removal via bag filters or sand media
3
Primary PFAS removal step (e.g., foam fractionation)
4
Chitosan-biochar contactor polishing (EBCT 10-30 min)
Quality Control
Monitoring & Verification
1
SPLP or LEAF methodology for verify stabilization & leachability
2
Target analyte tracking (PFOS, PFOA, PFHxS)
3
TOP assays for ensuring precursor immobilization
4
Groundwater trend analysis to monitor mass flux reduction
Dosage Specifications & Application Rates
Component
Dosage Range
Application Info
Target PFAS
Efficiency
Biochar (3mm)
2-5%dry wt
1-2 ft lift thickness
Long-chain (PFOS, PFOA)
99%
Chitosan (COS-HCl)
0.1-0.5%dry wt
0.1-0.2% solution conc.
Short-chain (PFBS, PFHxA)
>99.9%
Mass Ratio
1:10 to 1:20
1 part chitosan to 10+ biochar
All PFAS variants
98%+stabilization
Water Polishing (EBCT)
10-30 min
10-15 min optimal (pilot)
Recalcitrant PFAS
Guard bed
Dosage Efficiency
Copyright 2026 Shield Nutraceuticals/Chitosan Global
Contact: John Hott | Email: John@Chitosanglobal.com | chitosanglobal.com

## Slide 4
3mm Biochar
biocharnow.com
$385/cubic yard
Premium grade, 3mm particle size
Chitosan IG
chitosanglobal.com
$135/kg
Industrial grade, 98% purity
Dosage Ratio
Recommended
1:10-20 chitosan:biochar
By dry weight basis
Dosage Framework
Soil Application
Biochar (dry weight)
2-5%
of treated soil mass
Chitosan (dry weight)
0.1-0.5%
of treated soil mass
EBCT (Water)
10-30 min
Empty bed contact time
Mass Ratio
1:10-20
Chitosan:Biochar
* Dosages are starting points for pilot-scale testing. Site-specific conditions may require adjustment.
Component Structure
Dual Mechanism
COS-HCl
+71 mV charge
98% DDA
3 kDa MW
Biochar
3mm particle
High surface area
Stable scaffold
Chitosan component cost
$135/kg
Biochar component cost
$385/cubic yard
Typical application ratio
1:15
Cost & Component Reference
Pricing analysis for PFAS remediation platform
2026 Shield Nutraceuticals/Chitosan Global
Contact: John Hott | Email: John@Chitosanglobal.com | Website: chitosanglobal.com

## Slide 5
Traditional Systems
GAC (Granular Activated Carbon)
Primary PFAS removal; TOC/NOM shortens bed life
IX (Ion Exchange)
Competing anions reduce bed life; single-use resin common
RO/NF (Reverse Osmosis)
Concentrate residual adds disposal burden
Chitosan-Biochar Platform
Upstream immobilization/polishing step
Cost/Burden Analysis
GAC: TOC/NOM Impact
TOC/NOM shortens bed life, requiring more frequent media replacement
IX: Competing Anions
Competing anions reduce bed life; single-use resin common
RO/NF: Disposal Burden
Concentrate residual adds disposal burden and costs
Numeric Benchmarks
Tech | Cost | Unit
IX (2000 gpm) | $150,552 | annual
GAC (2000 gpm) | $269,790 | annual
IX (2000 gpm) | $0.14 | /1000 gal
GAC (2000 gpm) | $0.26 | /1000 gal
IX (500 gpm) | $0.26 | /1000 gal
GAC (500 gpm) | $0.45 | /1000 gal
Source: EPA, NEWMOA (2023)
Integrated chitosan-biochar platform: upstream immobilization/polishing step intended to reduce PFAS mass flux and protect downstream media life.
Water Treatment Cost Benchmarks
EPA PFAS treatment costs and performance analysis
Cost Analysis
Copyright 2026 Shield Nutraceuticals/Chitosan Global
Contact: John Hott
Email: John@Chitosanglobal.com
Website: chitosanglobal.com

## Slide 6
Conventional Pathways
Soil Washing
$100-$200/ton excluding residual treatment
Stabilization/Solidification
$100-$150/ton at 2% amendment
Smoldering Combustion
$260-$330/ton
Thermal Desorption
~$500/ton
Benchmark Ranges
Soil washing (25k tons)
$100-$200
/ton
Stabilization (2% amendment)
$100-$150
/ton
Smoldering
$260-$330
/ton
Thermal desorption
~$500
/ton
Platform Cost Structure
Chitosan IG
$135/kg
3mm Biochar
$385/cy
Biochar dosage
2-5% dry wt
Chitosan dosage
0.1-0.5% dry wt
Chitosan-only equivalent
$122-$612/ton
Integrated platform is positioned for immobilization and mass-flux reduction, not as a direct substitute for excavation plus thermal destruction.
Soil Remediation Cost Benchmarks
Cost analysis for PFAS soil treatment options
Cost Analysis
Copyright 2026 Shield Nutraceuticals/Chitosan Global
Contact: John Hott
Email: John@Chitosanglobal.com
Website: chitosanglobal.com